## Slide 1: 3D Printing
“Basic printer use, safety, and how not to fucking destroy our nice things holy fucking shit you guys!” ~Colin
By: Spencer K
&

## Slide 2: This will cover
3D Printing technologies
Modeling for 3D printing
Exporting models
Slicing your model
Setting up the 3D Printer
Printing
Monitoring
Finishing your print

## Slide 3: 3D Printing technologies
How to export your model to a standard format

## Slide 4: Three main types
Stereo lithography
  SLA or DLP
Binder Jetting
  Drop-on-powder
Fused Deposition Modeling
  FDM

## Slide 5: Stereo lithography
Light Reactive Fluid
Fluid tray
Bakes model to harden
Pros
  Extremely detailed prints
  Overhangs
Cons
  Messy
  Expensive
  Slow

## Slide 6: Binder Jetting
Powdered substrate
Liquid binding agent
Pros
  Infinite colors
  High detail
  Exotic materials
Cons
  Brittle until baked/cured
  Large machines

## Slide 7: Fused Deposition Modeling
PLA or ABS Plastic
Heated extrusion head
Pros
  Quick
  Relatively inexpensive
Cons
  Model design limitations
  Sensitive to environment
Notes: Like a robotic hot glue gun

## Slide 8: PLA
Not really food safe
Biodegradable
Don’t breathe this
Strong and rigid
Also hates the word moist
Notes: Keep the filament away from moisture.
Ask a 3da to show you how to change the filament

## Slide 9: Modeling for 3D printing
Tips to help you design a more robust part

## Slide 10: Things to avoid
Hard Edges
90º Overhangs
Non-Manifold geometry
  Single point connections
  Thin walls
  Open solids

## Slide 11: Design considerations
Holes will print slightly smaller
Outer diameters will print slightly larger
Organic surfaces will have layers

## Slide 12: Exporting your model
How to export your model to a standard format

## Slide 13: Export as an .stl
Make sure you have the correct units.
Export one part at a time

## Slide 14: Slicing your model
Generate the Gcode

## Slide 15: Download the MakerBot Desktop software
Makerbot.com/desktop
RIP Linux users.

## Slide 16: Set the device model
Select the Replicator 2 from the devices menu
  You will only have to do this once.

## Slide 17
Look
Move
Rotate
Scale
Settings
Export

## Slide 18: Lay flat

## Slide 19: Keep it inside the build area

## Slide 20: Convert from inches to millimeters
If your print shows up tiny in the build area.

## Slide 21: Settings
Three things you will change:
Infill
Support
Raft
Shells

## Slide 22: Rafts
Prints a thick layer first to overcome print bed roughness
Can hurt more than it helps
  Your mileage may vary

## Slide 23: Support
Provides a surface for new layers to print onto
Without it your prints may sag

## Slide 24: Infill
How solid the print is
10-20% is usually perfectly strong enough

## Slide 25: Number of Shells
Outer layers of the print
Unrelated to infill
More is stronger
  2 is usually fine

## Slide 26: Setting up the 3D printer
Preparing the print bed

## Slide 27: Level the build plate
THIS IS THE MOST IMPORTANT PART!

## Slide 28: Why leveling is important
Not enough pressure
Filament doesn’t stick
Print lifts off and fails
Good contact
Filament is lightly spread out
Ideal
Too much pressure
Filament can’t flow
No good

## Slide 29
Too close
Too far

## Slide 30: Leveling the build plate
Home Axes
Notes: Go down to utilities
Enter, go to Home axes

## Slide 31: Leveling the build plate
Locate screws

## Slide 32: Leveling the build plate
Level front LEFT

## Slide 33: Leveling the build plate
Level front RIGHT

## Slide 34: Leveling the build plate
Level the BACK

## Slide 35: Leveling the build plate
Paper should touch but freely move back and fourth.

## Slide 36: Why leveling is important
Not enough pressure
Filament doesn’t stick
Print lifts off and fails
Good contact
Filament is lightly spread out
Ideal
Too much pressure
Filament can’t flow
No good
  SHEET OF PAPER

## Slide 37: Printing
What you actually came here to do.

## Slide 38: Check the filament
Make sure you won’t run out
No automated way of knowing how much is left

## Slide 39: Print your model

## Slide 40: Watch the first layer
If it isn’t even and clean, you are gonna’ have a bad time.

## Slide 41: DON’T TOUCH IT
Notes: You’ll just fuck it up (the print, your fingers, or the printer)

## Slide 42: Monitoring
Checking in on your print

## Slide 43: Keep an eye on it
Stay and watch the first layer complete
Watch the stream online:
  thundercam.csh.rit.edu/video.cgi

## Slide 44: Finishing your print
Removing and cleaning your 3D print

## Slide 45: Remove the build build plate
Push back, then lift the front.
lift
lift
2
2
1
Push back

## Slide 46: Remove print from build plate
Start at the corner and slowly pry like you’d turn a key.

## Slide 47: Cleaning support and fluff
Manicure tools work very well.

## Slide 48: Recap
If you’ve been asleep for the entire presentation, wake up and remember this part.

## Slide 49: Keep it inside the build area

## Slide 50
Level
The
Build plate

## Slide 51: DON’T TOUCH IT
While it’s moving, hot, or otherwise doing its thing.
Notes: You’ll just fuck it up (the print, your fingers, or the printer)

## Slide 52: 3D Admins
Me:
goblin@csh.rit.edu
spencerk@csh.rit.edu
Fish 3049
The Research Room
Brick City @ lunchtime
Other 3DAs:
3da@csh.rit.edu
Colin O. @faokryn
Drew G. @dag10
Marc B. @mbillow
Max B. @maxime
Trevor S. @sherrardtr